Structure of book

Workbook
└ solver
sheet for solver
The solver is ran by VBA automatically when calculation of book is executed.

└ SystemModel
sheet for model of physical system, ex, Heat circuit
equivalent to model diagram in OpenModelica.

└ Lib_HeatTransfer
sheet to store the “components” for system modeling
equivalent to library package in OpenModelica.

└ ExtrT
sheet for visualizing temperature distribution

└ ExtrQ
sheet for visualizing heat flow through each conductive component.

How physical systems of equations are solved

Commence

Solver updates independent variables
Components in system model executes calculation of physical model with given independent variables.
The calculated dependent variables in system model are sent to solver.
The solver evaluates Jacobian matrix with calculated dependent variables.
 → sheet: solver
 → sheet: SystemModels

 dependent variables are “sum of flow”, ex sum of heat out of heat circuit node, in most of cases.

 → sheet: SystemModels

→ sheet: solver

 independent variables are “potential” of nodes, ex temperature of node, in most cases

Systems of equation converged?

false

True

End

1. Components in Lib_HeatTransfer
  1. Conduction
A component which simulates conductive heat resistance.

Icon with auto-shape

“Connector”
  Input / output with other component instances.

Component’s internal calculation

    1. input / output
      1. input
T1 [K]: temperature at connector 1
T2 [K]: temperature at connector 2

A [m2]: area of heat transfer
th [m]: distance of conduction
lambda [W/(m*K)]: heat conductivity

      1. output
Q1in [W]: heat flow into connector 1
Q2in [W]: heat flow into connector 2

  1. NodeSS

    1. input / output
      1. input

      1. output

  1. ****

    1. input / output
      1. input

      1. output

****

****